## Slide 1
23CCE381 / 23ECE381 | Open Laboratory - I | Review 2
HYPERSPHERE ENGINE
Decentralized IoT Edge Biometric Attendance & Campus Geofencing System
TARGET HARDWARE
Raspberry Pi 4 / 5 (ARM64)
CLIENT DEVICES
Smartphones (BYOD)
ML MODELS
4 Neural Networks < 25 MB
LATENCY
< 200ms End-to-End
NIT Trichy (CDI) & Amrita Vishwa Vidyapeetham
Notes: Title slide. Introduce the project name, course code, and Review 2 context. Emphasize that this is an IoT edge system running entirely on Raspberry Pi hardware with zero cloud dependency. Mention the sub-200ms latency target.

## Slide 2
02 | PROBLEM STATEMENT
Why Edge IoT Beats Cloud-Based Biometrics
CLOUD-BASED BOTTLENECKS
High Network Latency: Uploading hi-res face images to cloud creates >1.5s delays and consumes institutional bandwidth
Privacy & Compliance Violations: Storing biometric templates on 3rd-party cloud infrastructure risks data leakage
Single Point of Network Failure: Internet disruption halts the entire campus attendance system
HYPERSPHERE IoT EDGE SOLUTION
Edge Computing Gateway: Complete ML inference and vector matching execute locally on Raspberry Pi 4/5
Zero-Cloud Architecture: Works offline over local campus Wi-Fi or LAN - no internet dependency
BYOD Interaction: Faculty/students use personal phones to mark attendance - no touchpoints or queue bottlenecks
Notes: Present the three major problems with cloud-based biometric attendance, then contrast with the three IoT edge solutions. Emphasize zero cloud costs, data sovereignty, and offline resilience.

## Slide 3
03 | SYSTEM ARCHITECTURE
End-to-End IoT Edge System Design
MOBILE SMARTPHONES
Mobile Web Browser (PWA)
Client-side MediaPipe Vision
Hardware GPS Fix for Geofence
Camera Capture & Blink Detection
Local Campus Wi-Fi / REST
RASPBERRY PI 4/5 GATEWAY
Next.js 15 (Edge UI Server)
FastAPI (Async Python ASGI)
Low-Power: 5V / ~7.5W
EMBEDDED ML PIPELINE (ARM64)
1. SCRFD-2.5G ONNX (Detection)
2. Quality Gating & Affine Align
3. MiniFASNetV2 Anti-Spoofing
4. ArcFace MobileFaceNet (Embed)
EDGE STORAGE
SQLite + In-Memory
pgvector HNSW Index
Ray-Casting PiP
103 Building Polygons
Geofence Engine
Notes: Walk through the 3-tier architecture: Mobile clients -> Raspberry Pi Edge Gateway -> Local embedded ML pipeline -> Edge vector DB and geofence engine. Emphasize zero cloud dependency and local campus Wi-Fi connectivity.

## Slide 4
04 | EMBEDDED ML PIPELINE
Lightweight Model Selection for ARM64 Edge
Pipeline Stage | Model | Parameters | Memory | ARM64 Acceleration
1. Face Detection | SCRFD-2.5G (ONNX) | 0.67M | 3.2 MB | ONNX ARM NEON SIMD
2. Alignment | 5-Point Partial Affine | Analytical | < 1 KB | OpenCV ARM Optimized
3. Anti-Spoofing | MiniFASNetV2 (PyTorch) | 0.43M | 1.8 MB | PyTorch CPU (Quantized)
4. Feature Extractor | ArcFace MobileFaceNet | 1.2M | 13.6 MB | ONNX Runtime INT8/FP32
5. High-Res Alt | ArcFace ResNet-50 | 43.6M | 174 MB | FP32 (High precision)
KEY INSIGHT
Total memory footprint: < 25 MB for ALL neural network weights combined! Fits easily into Raspberry Pi's 4GB/8GB RAM with >90% headroom.
Notes: Walk through each pipeline stage and explain model selection rationale. Emphasize that ALL models combined use less than 25MB - perfect for RPi edge deployment. Contrast MobileFaceNet (13.6MB) vs ResNet-50 (174MB) and why MobileFaceNet is the primary choice.

## Slide 5
05 | MATHEMATICAL ALIGNMENT
Quality Gating & 5-Point Affine Normalization
5-POINT AFFINE NORMALIZATION
Extracts 5 facial anchors: Left Eye, Right Eye, Nose Tip, Left Mouth, Right Mouth
Maps to ArcFace canonical coordinates DST_PTS: [30.29, 51.70], [65.53, 51.50], [48.03, 71.74], [33.55, 92.37], [62.73, 92.20]
Eliminates roll angle & perspective distortion
Yields aligned 112x112 crop for embedding extraction
EDGE QUALITY GUARDS
Laplacian Focus Blur: Var(Laplacian) >= 50.0 Rejects blurred captures from moving phones
Luminance Bounds: mean_gray in [40.0, 220.0] Prevents underlit or overexposed frames
3D Head Pose (solvePnP): |yaw| < 30 deg, |pitch| < 25 deg Rejects extreme angles for accuracy
Notes: Explain 5-point affine alignment as a critical preprocessing step. The DST_PTS canonical coordinates ensure consistent face geometry regardless of capture angle. Quality guards save CPU cycles by rejecting bad frames before running expensive neural networks.

## Slide 6
06 | PRESENTATION ATTACK DEFENSE
MiniFASNetV2 Anti-Spoofing on Edge Hardware
THE THREAT
Attackers holding up printed photos or replaying face videos on smartphone screens to spoof biometric verification
MINIFASNETV2 DEFENSE MECHANISM
Evaluates 2.7x expanded crop (80x80 RGB) to capture peripheral depth gradients & moire patterns
Generates softmax liveness probability: P(Live Face) >= 0.40 threshold
Rejects screen replays & printed photos in < 40ms on ARM Cortex-A72/A76
99.12%
Accuracy
0.88%
ACER
< 40ms
Inference
0.43M
Parameters
Notes: Explain the presentation attack defense layer. MiniFASNetV2 uses an expanded 2.7x crop to capture texture artifacts from digital displays (moire patterns) and printed photos. Achieves 99.12% accuracy on CASIA-SURF benchmark with only 0.43M parameters.

## Slide 7
07 | PERFORMANCE BENCHMARKS
Raspberry Pi Latency Budget, Thermal & Power Profile
Pipeline Stage | Duration | Cumulative
Phone Image Capture & Tx | 20 ms | 20 ms
SCRFD Face Detection | 42 ms | 62 ms
Quality & Affine Alignment | 5 ms | 67 ms
MiniFASNetV2 Liveness | 38 ms | 105 ms
ArcFace MobileFaceNet Embed | 32 ms | 137 ms
Vector Similarity Match | 2 ms | 139 ms
RPi 5 TOTAL
~139ms
RPi 4 TOTAL
~215ms
HARDWARE POWER & THERMALS
Power Draw: 5V, 1.5A = ~7.5W under full inference workload
Thermal Equilibrium: 48-54 C with passive aluminum heatsink
No active cooling required for sustained inference operation
Notes: Break down the end-to-end latency budget for each pipeline stage. Total verification is ~139ms on Pi 5 and ~215ms on Pi 4. Highlight the low power draw (7.5W) and stable thermals (48-54C) with passive cooling only.

## Slide 8
08 | CAMPUS GEOFENCING
Hierarchical GPS Geofencing & Location Verification
TIER 1: INSIDE BUILDING
Ray-Casting Point-in-Polygon (PiP) checks GPS against 103 OSM building polygons in < 1ms
TIER 2: CAMPUS GROUNDS
Verifies user is within the outer campus perimeter boundary polygon
TIER 3: OFF CAMPUS
Rejects or flags attendance record for manual administrator review
HARDWARE GPS ENFORCEMENT
Rejects IP-based location fixes (accuracy radius > 100m). Requires true mobile device hardware GNSS/GPS fixes for secure geoverification. Jordan Curve Theorem (Ray-Casting PiP) evaluates 103 polygons in < 1.2ms on ARM.
Notes: Explain the 3-tier hierarchical geofencing system. Tier 1 uses the Jordan Curve Theorem (ray-casting PiP) to check if GPS coordinates fall inside any of the 103 campus building polygons from OpenStreetMap. Hardware GPS enforcement ensures IP-based spoofing is blocked.

## Slide 9
09 | LIVE DEMO
Proof-of-Concept Demonstration Workflow
1
MOBILE ACCESS
Open http://<edge-ip>:3000 from phone browser
2
ROLE-BASED AUTH
Login as faculty (hodece) or admin (director, kv)
3
FACE CAPTURE
User captures face Blink detected as liveness
4
EDGE PROCESSING
Pi processes: Detection, Anti-Spoof, Embedding
5
RESULT
Attendance confirmed with building name in < 200ms
LIVE ANTI-SPOOFING DEFENSE
Displaying a face photo on another phone triggers instant rejection: "Spoof detected: Liveness score 0.12"
ADMIN EDGE TELEMETRY
Shows CPU temperature, RAM usage (only 280MB used), multi-embedding drift logs, and real-time inference metrics
Notes: Walk through the 5-step live demo workflow. Demonstrate the anti-spoofing defense by showing a photo on another phone. Show the admin telemetry dashboard with CPU temp and RAM metrics from the Pi.

## Slide 10
10 | CONCLUSION & ROADMAP
Review 2 Milestones & Review 3 Target
REVIEW 2 MILESTONES ACCOMPLISHED
Complete IoT edge architecture designed and validated on Raspberry Pi hardware
Multi-stage embedded ML pipeline optimized for ARM64 with sub-200ms turnaround
Working proof-of-concept running with mobile phone interaction over local Wi-Fi
4 neural networks totaling < 25MB memory footprint with 99.12% anti-spoof accuracy
103 campus building geofence polygons with < 1.2ms PiP evaluation
REVIEW 3 TARGET (OCTOBER 22, 2026)
Custom 3D-printed Raspberry Pi kiosk enclosure with OLED status display & buzzer
Offline sync buffer with MQTT telemetry for multi-device mesh communication
Academic poster presentation layout and final viva defense preparation
Extended evaluation with 50+ concurrent users on campus for stress testing
INT8 quantized model optimization for further latency reduction on Pi 4
Thank You | Questions & Discussion
Notes: Summarize the Review 2 achievements and present the Review 3 roadmap. Invite questions from the evaluation panel. Key talking points: IoT edge architecture, sub-200ms latency, zero cloud dependency, and the upcoming 3D-printed kiosk hardware integration.